## Slide 1: Software NEWS
What’s new since the last technical meeting November 2021?
Technical meeting 2022 Lutz Augenstein

## Slide 2: Agenda
Electronic cam disc
Important and highlights 6.5-G
Outlook

## Slide 3: Electronic cam disc

## Slide 4: Electronic cam disc
6.5-G
  „Same“ situation as technical meeting 2021 =
Outlook
  Sales release not clear
  Technical future not clear
    „The further development of the IGB is discontinued”
Notes: SD6 no longer in focus
Maybe cam disc will canceled, removed from software

## Slide 5: 6.5-F 6.5-G

## Slide 6: 6.5-G / 6.5-G SP1
F becomes G
  F = feature release (withdrawn); planned for 12/2021
  G = „ unofficial service pack for F“ (FW, App, DS6)
  G SP1 = official service for G (only DS6)
> 100 improvements, for example
PROFIdrive IRT AC4
EZ2
Online help and translations
Graphical programming
EtherCAT Feature: Diagnosis History
Virtual Lifetime
SSI encoder evaluation

## Slide 7: Online help and translations

## Slide 8: Online help
New: Integrated online help
  For all tool functions, except:
    Graphical programming (under work)
    PASMotion (has its own help integrated)

## Slide 9: Online help
Context sensitive
  For wizzard pages partially

## Slide 10: Translations
Tool GUI is translated with every version (excluding parameter names)
6.5-G: Big update of parameter descriptions (de) and complete translation (en-us, fr)

## Slide 11: Graphical programming

## Slide 12: Graphical programing – new functions
Description of own program blocks
Notes: Also for local blocks

## Slide 13: Graphical programing – new functions
Using parameters in own library blocks
Quiz: Where is the definition source of the parameter?

## Slide 14: Graphical programing – new functions
P01

## Slide 15: Graphical programing – new functions
I80

## Slide 16: Graphical programing – new functions
P00

## Slide 17: Graphical programming – new functions
Using own axis dependant parameter in double axis drive controller

## Slide 18: Graphical programming
Licenses for customers
Procedure, ERP/SAP and financial details are ready
  Order department (Germany, Mr. Weber AT, Mrs. Grasso CH, Mrs. Matitch FR)
  Variant 1: Purchase variant, Company version
    Gross price 4000 €
    Unlimited number of users
    Unlimited validity
    1 day training for 2 participants included
  Variant 2: Test version
    Limited to 90 days
Documentation under work
  Online help extension planned
Sales release yes/no?: not clear
  Maybe sales starts without explicit sales release
Notes: SAP: DS6_LICENSE or DS6_EVAL_LICENSE (Test license = free of charge)

## Slide 19: EtherCAT Feature Diagnosis History

## Slide 20: EtherCAT Feature: Diagnosis History
New EtherCAT diagnostic memory in the drive controller
  Firmware 6.5-F or higher required
  New communication object Diagnosis History 10F3 hex
Contains the last 20 diagnostic events
  Only fault events = Emergency telegrams
  Volatile data, will be deleted with every drive controller restart
Display of diagnostic messages with text in the EtherCAT-Master
  ESI created with DS6 6.5-G or higher
  Languages german, english, french

## Slide 21: EtherCAT Feature: Diagnosis History

## Slide 22: Virtual Lifetime

## Slide 23: Virtual Lifetime
Monitoring
  Precisely detect drive conditions
Predictive Maintanance
  Maintaining foresight
Drive Optimization
  Sustainable management
New features will present in the campaign Virtual Lifetime

## Slide 24: Virtual Lifetime / Predictive Maintanance - roadmap
Analytical-physical approach
Predicts the causes of damage containded in the model
The state of the gear unit is assessed by means of the measured actual values using algorithms
STÖBER
predictive maintenance
Model-based approach
Spectrum-based approach
Deep learning approach
V 1.X
V 1.2
V 1.0
V 2.0
V 3.0

## Slide 25: Virtual Lifetime - overview
Version 1.0 (DS6 V 6.5-G / May 2022)
Model based approach (Analytical-physical approach)
Focus: STÖBER geared motor
Predicts the causes of damage contained in the model
Using measured actual values, a life performance indicator is calculated via physical-technical equations
Uses existing STÖBER system components
Actual only non cascaded gear units
Requires no additional sensors
No customer know-how required, no parameterization necessary

## Slide 26: Virtual Lifetime - overview
Requires no additional sensors, cables or components
  Predictive Maintenance is free of charge for our customers
This solution is realized exclusively in the firmware
  G6 drive controller; FW + configuration 6.5-G or higher
Predictive Maintenance is always automatically activated (normal case)
  Gear motors with electronic nameplate, manufactured may 2022 or later
  Only for gear units series
    C, generation 0
    F, generation 0
    K, generation 0
    P, generation 3
    PH, generation 3
    S, generation 0

## Slide 27: Virtual Lifetime - overview
Our customers get direct access to their collected data base via parameter
  PLC program blocks for Beckhoff / Siemens in preparation
The solution provides a clear recommendation for action/maintenance via parameter - customer does not need any evaluation know-how
Fully integrated in the STÖBER system
  Geared motor types ASM, SSM, LM

## Slide 28: Virtual Lifetime - overview
speed / torque/ temperature / …
Geared motor reference values
algorithm
Recommendation change geared motor
Life performance
indicator
Load matrix
Status
6. Generation
0%  100%  100%+
TOP SECRET
TOP SECRET

## Slide 29: Recommendation change geared motor
Parameter R100 PM State
0: Inactive
Predictive Maintenance is not activated or no STÖBER system
1: Active
Predictive Maintenance is activated The drive is monitored
2: Recommendation geared motor replacement
Replacement of the geared motor is recommended; the life performance indicator has reached a value ≥ 90% (source: R101)

## Slide 30: Life performance indicator
R101 PM LLI

## Slide 31: Life performance indicator
Values below 100% mean that the gearmotor is within its lifetime performance
If the value is closer to 100% or above, the probability of failure increases
  Increasing values do not mean that there is damage to the gearmotor
Even with values above 100%, operation can continue
Values is saved in the power unit
  Additional at SD card/Paramodul every 10 min
  Independent from A00
Consideration of the temperature
  If motor temperature sensor available (KTY/PT)

## Slide 32: Load matrix
Recording of the duration of the speeds and torques that have occurred at the output of the gearmotor over the operating time
The load matrix describes the summed duration for defined load classes. A class is characterized by a speed and torque range assigned to it.
  Torque: 31 buckets
  Speed: 21 buckets
The load matrix is a statistical data base, the reconstruction of the motion profile is not possible
Values are saved ONLY in the SD card/Paramodul
  Every 30 min
  Independent from A00

## Slide 33: Load matrix - principle
Speed
Torque
Motion profile

## Slide 34: Load matrix - principle
Speed
Torque
Class-interval
speed
Class-interval
Torque
Speed class
Torque class
Equidistant classes formation
Equidistant Sampling of Speed and Torque
Determine the associated class
Sampling interval

## Slide 35: Load matrix - principle
Speed
Torque
Class-interval
speed
Class-interval
Torque
Speed class
Torque class
Sampling interval
Class Torque
Class Speed
Duration in the class
Class
Count

## Slide 36: Load matrix - access
*.csv

## Slide 37: Load matrix – SD card
\PRM\<filename>
0AF776B2.P00
Motor serial number
P = Predicitve Maintenance
0 = Primary file
0 = Axis A
ED212U.P00
File name without „encoder“:
Example:

## Slide 38: Load matrix – *.csv
...
"t-average":
[-2.500000,-2.333333,-2.166667,-2.000000,-1.833333,-1.666667,-1.500000,-1.333333,-1.166667,-1.000000,0.833333,-0.666667,-0.500000,-0.333333,-0.166667,-0.000000,0.166667,0.333333,0.500000,
0.666667,0.833333,1.000000,1.166667,1.333333,1.500000,1.66666, 7,1.833333,2.000000,2.166667,2.333333,2.500000],
"t-average-unit": "%",
"n-average":
[-900.000000,-810.000000,-720.000000,-630.000000,-540.000000,-450.000000,-360.00000,0,-270.000000,-180.000000,
-90.000000,0.000000,90.000000,180.000000,270.000000,360.000000,450.000000,540.000000,630.000000,
720.000000,810.000000,900.000000],
"n-average-unit": "rpm",
"load-matrix":
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, ],
...
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, ],
[0, 0, 0, 0, 1000, 3000, 4000, 4000, 3000, 4000, 1000, 0, 0, 0, 0, 0, 0, 0, 0, 0,0, ],
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, ],
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 2000, 4000, 4000, 3000, 4000, 3000, 0, 0, 0, 0,0, ],
. . .
[0, 0, 0, 0, 0, 3000, 4000, 4000, 3000, 4000, 2000, 0, 0, 0, 0, 0, 0, 0, 0, 0,0, ],
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, ],
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 1000, 4000, 4000, 3000, 4000, 3000, 1000, 0, 0, 0,0, ],
[0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, ],
...

## Slide 39: Load matrix
Chart: Speed buckets
| -900 | -810 | -720 | -630 | -540 | -450 | -360 | -270 | -180 | -90 | 0 | 90 | 180 | 270 | 360 | 450 | 540 | 630 | 720 | 810 | 900
-250% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-233% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-217% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-200% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-183% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-167% | 0 | 0 | 0 | 0 | 1000 | 3000 | 4000 | 4000 | 3000 | 4000 | 1000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-150% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-133% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2000 | 4000 | 4000 | 3000 | 4000 | 3000 | 0 | 0 | 0 | 0 | 0
-117% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-100% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-83% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
-67% | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 40: Load matrix - use cases
Product optimizations
Recognition of the real load situation of machines
Recognition of "borderline" machine designs
Improvements in the direction of quality and/or economic efficiency possible
Service
Assessment of above-average or below-average stress on machines
Detection of "borderline" applications
Detection of faults in the overall system

## Slide 41: Wizzard Predictive Maintenance
Predictive Maintenance state
Send load matrix to Stöber
Manual configuration
Recommendation change geared motor
Export for analysis, e.g. Excel

## Slide 42: Wizzard Predictive Maintenance - Manual configuration
Don‘t forget: A00 and restart neccessary

## Slide 43: SSI encoder evaluation

## Slide 44: SSI encoder evaluation
Synchronous Serial Interface (SSI)
A synchronous, point to point, serial communication channel for digital data transmission
CLOCK and DATA signals are transmitted according to RS-422, also known as ANSI/TIA/EIA-422-B
How does it work?
Drive controller creates the CLOCK
Encoder answers with DATA

## Slide 45: SSI encoder evaluation - comparison
 | Generation 5 | Gen 6 up to 6.5-E | Gen 6 from 6.5-G
Data length [bit] | 13, 24, 25 | 13, 24, 25 | 8 – 32
Position meaning | Fixed 13 ST or 12 ST+12MT or 13 ST+12MT | „Scalable“ same as G5 possible, other with restrictions | Scalable
Clock frequency [kHz] | 250 / 600 | 250 / 600 | 150 – 1000
Time for 1 bit [us] | 4 / 1.67 | 4 / 1.67 | 6.67 – 1,67
Monoflop time [us] | „30“ | 30 | 10 - 100
Alarm bit suppport | no | no | yes
Requirements terminal module | „nothing“ | nothing | XI6: from HW 14 RI6: from HW 8

## Slide 46: SSI encoder evaluation - comparison
 | Generation 5 | Gen 6 up to 6.5-E | Gen 6 from 6.5-G
Data length [bit] | 13, 24, 25 | 13, 24, 25 | 8 – 32
Position meaning | Fixed 13 ST or 12 ST+12MT or 13 ST+12MT | „Scalable“ same as G5 possible, other with restrictions | Scalable
Clock frequency [kHz] | 250 / 600 | 250 / 600 | 150 – 1000
Time for 1 bit [us] | 4 / 1.67 | 4 / 1.67 | 6.67 – 1,67
Monoflop time [us] | „30“ | 30 | 10 - 100
Alarm bit suppport | no | no | yes
Requirements terminal module | „nothing“ | nothing | XI6: from HW 14 RI6: from HW 8

## Slide 47: SSI encoder evaluation - How does it work?

## Slide 48: SSI encoder evaluation - How does it work?

## Slide 49: SSI encoder evaluation – example – new variant
Using a 18 bit ST encoder, without alarm bit:
Select encoder function 78
Set data bit length to 18
Set scaling to 262 144 LSBs (218)
If possible:
Transmission time < control cascade cycle
Increase H15 / reduce H17 (! encoder spec)
Deavtivate H11 (loss data security)
The preferred, new & perfect variant

## Slide 50: SSI encoder evaluation – example – old variant
Using a 18 bit ST encoder, without alarm bit:
Select encoder function 65
Set data bit length to 24
Set scaling to 16 777 216 LSBs (224)
18 bit available, but 24 read out???
The old, tricky variant (especially for MT)

## Slide 51: SSI encoder evaluation – example –old variant
18 bit available, but 24 read out???
1
ST
217
2
ST
216
17
ST
21
18
ST
20
19
ST
217
20
ST
216
23
ST
213
24
ST
212
24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
useful data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | „Noise“ |  |  |  |  | 

## Slide 52: Outlook

## Slide 53: Outlook - Configurator accessories

## Slide 54: Outlook - Configurator accessories

## Slide 55: Outlook –„6.5-H“
Planned improvements: ~50
Planned completion: „11/2022“
Main focus: –
Product maintenance
  PROFIdrive: support for other TA
  Online help: graphical programming and program blocks
  …