## Slide 1: Play it safe with the STOBER SD6 drive controller
High-performance control of synchronous and asynchronous motors. Flexible application with extensive safety functions.
Safety technology in cooperation with

## Slide 2: BETTER SAFE THAN SORRY
What happens in case of service?
Are your movements safe?
Are your vertical axes and their brakes safe?
Are your safety functions flexible enough?
Do you have to sacrifice performance or availability because of safety technology?

## Slide 3: STOBER Safety Philosophy
How you benefit
Simple and complete protection
Protection against incorrect operation
Protection in the event of malfunctions
Flexible basis for solutions
No added costs in case of service
High level of protection for machines and investments
  Good safety technology the STOBER way
Close to the customer
Targeted protection according to the standard
Fast reaction times
High level of availability
Quick and easy commissioning
Straightforward operation
Our concept
Maximum safety
Strong practical orientation
High efficiency
Huge range of functions
More flexibility

## Slide 4
Play It Safe
Safe, efficient and flexible with the SD6
Practice-oriented solution for safe vertical axes!
Always on the safe side with SIL 3, PL e (cat. 4)!
Free selection of motors, encoders and cables! Ideal for retrofitting.

## Slide 5: The New Safety Generation: SD6 with SE6 Safety Module
You save space, time
and money!
We guarantee a reaction time of 10 ms at the highest safety level!
Free motor and encoder selection
No error elimination necessary for attaching the encoder
Simple digital encoder cable, no sin/cos adapter
Elimination of stall/speed monitor
Straightforward project configuration and commissioning
Simple, quick service concept

## Slide 6
SS1 and 10 additional, freely combinable safety functions at the highest level of safety!
SE6: Extensive Safety Functionality
Safe shutdown | Safe limiting | Safe position | Brake management
SOS
SLI
SLP
SDI SLS
SSR
Fallback level SS1! A controlled shutdown is smarter than just stopping – and faster!
STO
SS1
SS2
SIL 3, PL e (cat. 4)
SBC
SBT

## Slide 7: Safe Shutdown
SS2 – Safe stop 2
Monitored braking with transition to SOS
Detects errors while braking
Ideal for coupled axes and fast restarting
SS1
Sxx
STO – Safe torque off
Safe shutdown of the drive controller
Switches off the energy supply to the motor safely.
Ideal for safe restart lock
SOS
SS1 – Safe stop 1
Monitored braking with transition to STO
Fallback level for all safety functions
Detects errors while braking
Ideal for low safety distances

## Slide 8: Safe Limiting
SDI – Safe direction
Locking of a direction of motion
Configurable tolerance range
Ideal for limit switch monitoring
SLS – Safely-limited speed
Symmetrical monitoring at max. permitted speed
Optionally includes dynamic tolerance
Ideal for monitoring and commissioning
SSR – Safe speed range
Freely selectable upper and lower speed limit
Optionally includes dynamic tolerance
Ideal for speed range monitoring
SS1
SS1
SS1
Dynamic tolerance window

## Slide 9: Safe Position Monitoring
SLI – Safely-limited increment
Safely monitored increment
Single-ended motion limits
Ideal for variable position monitoring
SLP – Safely-limited position
Safe position range
Tests the absolute position for plausibility
Ideal for constant location monitoring
SS1
SS1
SOS – Safe operating stop
Monitored stall
Drive remains under control
Ideal for quickly restarting when loading and unloading
SS1

## Slide 10: Safe Brake Management
SBT – Safe brake test
Safe Brake Test
Individually configurable test process
No obligation of documentation
Ideal for gravity-loaded axes
SBC – Safe brake control
Safe Brake Control
Optional for one or two brakes
Regardless of brake type
Short circuit and cable break monitoring
Ideal for gravity-loaded axes
SS1
SS1
Grind brake
Refresh instead of replace
Automatic bedding of brakes
Ideal for increasing machine availability

## Slide 11: Possible Responses to a Detected Limit Value Violation
  SS1 – Controller-controlled
    Ideal for the controlled, monitored stopping of coupled axes by the function controller
  SS1 – Drive-controlled
    Ideal for the direct, controlled stopping of individual axes by the SE6 safety module
  Monitoring – Safe reporting
    Ideal for variable safety responses in complex systems
    Ideal for constant system protection
+
Safe limiting: SLS-M, SSR-M, SDI-M
Safe positioning: SLI-M, SLP-M, SOS-M

## Slide 12: Reaction Time as a Quality Criteria
SS1/SS2 Position-monitored
SS1/SS2 Time-monitored
Standard
STOBER
We guarantee a reaction time of 10 ms at the highest safety level!

## Slide 13: Easily and Quickly Put the System into Operation
DriveControlSuite project configuration and commissioning software
Efficient in both single and multi-axis applications
Wizards for convenient project configuration, parameterization and configuration
Safety configuration using the drag-and-drop principle
Integrated 12-channel oscilloscope
Removable data storage for simple series commissioning and service

## Slide 14: The Simple Service Concept
Exchange the SD card
Confirm
Test
… and that's it!
No special skills required!

## Slide 15: High Performance and Flexibility with the SD6
Isochronic system bus (IGB)
Flexible DC link connection using Quick DC-Link
A convenient operating unit consisting of graphical display and keys
Paramodul removable data storage for quick commissioning and efficient service
Practice-oriented safety technology
Control of linear and rotary synchronous servo motors and asynchronous motors
Large range of standard functions for controller- and drive-based applications
Universal options
Single-axis controller with nominal output current up to 85 A

## Slide 16: The Right Solution for You
Controller based
Drive based
in accordance with CiA 402

## Slide 17: Flexible DC Link Connection and Parameterization
Fieldbus
Fieldbus for external controller
  EtherCAT
  PROFINET
Integrated device bus (IGB)
Quick DC-Link
Quick DC-Link
Service interface and isochronic system bus (IGB)

## Slide 18: Passgenau mit modularem Schnittstellenkonzept
STOBER motors and gear units
Universal options

## Slide 19: BETTER SAFE THAN SORRY
Safe
Extensive safety functionality
Safe brake management
SIL3, PL e (cat.4) for all safety functions
Flexible
Manufacturer-neutral interfaces
Freely combinable safety functions
Simple service concept
Safe monitoring
Controlled shutdown
Efficient
Use of existing options
Fast response
Prevention of false triggering
Constant monitoring
Quick and easy commissioning

## Slide 20: BETTER SAFE THAN SORRY
SAFE
FLEXIBLE
EFFICIENT
Play it safe with the SD6 drive controller!