## Slide 1: sensorShift Wireless Module + PSGearStudy App
Introduction

## Slide 2: Agenda
Introduction
sensorShift Basics
Wireless Module
The App
Connection
  Android
  Windows
Live presentation
Best practice
Next steps

## Slide 3: Introduction
Study was introduced in 2020 -> STOBER Future Products Purpose:
  building a Bluetooth test platform
  Developing an easy-to-use interface for sensorShift service
  Gaining knowledge
  Paving the way for wireless connection to drive controllers…
Beta Software now ready for roll out
  Same code and GUI for different platforms
This Module is a functional prototype
  We have build 20 pieces for field testing

## Slide 4: sensorShift PCB
Microcontroller
32bit 48MHz
ARM M0+
Status LEDs
Relais for
PLC Feedback
Motor driver
Angular hall sensor
Connectors for motor and I/O signals
Service Port
Non-volatile memory

## Slide 5: User Interface vs. Available information
Status LEDs
-> Position
-> Error state
max-memorized values -> temperature -> voltage…
Production data -> Serialnumber -> Software Version
Switching statistics
fault memory
Fault counters
Visible for customer
Access only through test system
Manual for LED decoding:

## Slide 6: Wireless Module
Connects to sensorShift Translates BLE <-> sensorShift
Works with ANY sensorShift Firmware Version
No password required
No hot plugging -> Power off required before connection
Microcontroller
Bluetooth Chip
Interface to SensorShift Service Port

## Slide 7: Wireless Module - connection
Connection:
  Android
    visible in Bluetooth connection dialog
    No user action required (no pairing)
  Windows
    Pairing required („Add bluetooth devices“)
Will be detected as „SGAxxxxxxx“

## Slide 8: Wireless Module - LEDs
BLE State | BLE State 1 | BLE State 2
Waiting for connection | Blinking | off
connected | On | off
Discovered (ready for communication) | on | on
 | sensorShift Status
Try to connect to sensorShift | Off
Connection to sensorShift established | On
Green:
sensorShift connection Status
Yellow:
BLE State 1 & 2

## Slide 9: PS Gearstudy App
Service-Tool to read all relevant data
  Status
  Production information
  Pending Error messages
  Reading stored information
    Error counters
    Error memory
Multi-Platform Software
  Same GUI for Android and Windows
  iOS not supported yet
Beta Version
  Next update expected in May
  Share-Function will be added
  Stability issues in Windows will be solved
  …
  Please report all feedback to
  Martin.vetter@stoeber.de

## Slide 10: Android Software
App can be found in Google play store
Name must be written exactly (not case sensitive)
App should be available worldwide (we are working on availability in China) APK-File for direct installation
Android 9 or later required
Permissions crucial! -> “Location” needed for Bluetooth Without permission, no connection can be established There will be no error messages! If problems still occur, additional permissions for Android-internal functions might be missing (e.g. “Google Play Services”)

## Slide 11: App – Connection dialog
sensorShift power on
1. Select device
2. connect

## Slide 12: App -Dashboard
Signal strength
Position
One screen for most important informations
Updated ~every second
LED feedback like on PCB

## Slide 13: App - screens
disconnect
Dashboard
data
Fault memory
LED Identification
Settings

## Slide 14: Data - Statistics and memorized values
All data, stored in the sensorShift PCB
  Production data
  Switching Statistics
    Total switching cycles
    Failure rate
    Localizing shifting problems
    Check number of actuator repositioning (“anti-gear out function”)
  Max-memorized values
    Temperature
    …
  Fault counters
    Summing up all errors during lifetime
    23 different faults can be distinguished

## Slide 15: Fault memory
Press Update
All faults are listed
Press fault long

## Slide 16: Troubleshooting
Problem in Windows: Program might hang up after click on “Get connected”
Background: Connection-Settings to Wireless Module is stored in Windows When plugging to a different sensorShift PCB, there can be a problem when reconnecting Bluetooth
Solution: Remove Bluetooth device in Windows settings, then Add it again

## Slide 17: Live presentation

## Slide 18: Best practice - Dashboard
Check Switching failure rate (should be < 5%, depends also on external load)
Is input signal detected by sensorShift PCB?
Is actuator stuck at certain position?

## Slide 19: Best practice - Data
More in depth view
  Check Statistics
  Check fault counters

## Slide 20: Best practice – fault memory
Check last faults

## Slide 21: Next steps…
How to share Data?
Preffered:
  Using Sharepoint
Other possibilities:
  Teams
  Whatsapp
  Email