## Slide 1: PROFIdrive + PROFIsafe
Technical Meeting 2021 Part 1
16th november
For internal use only!
No release for public presentation.

## Slide 2: Agenda
PROFIsafe
Requirements
Adjustment and Usage
Commissioning / Live Demo
After the presentation you get the TIA Portal V17 examples for PROFIsafe and PROFIdrive and the necessary DS6 files.
Before we start, please give me a feedback with the hand symbol if you have experience with PROFIsafe.

## Slide 3: PROFIsafe – Requirements
1. Drive controller SI6 or SC6 (SD6 does not support PROFIdrive nor PROFIsafe)
2. At least firmware V6.5-D (TÜV)
3. TIA Portal 15 or newer
4. Additional software package - Step 7 Safety Advanced or Basic (depending on PLC)
5. Siemens Failsafe PLC (recognizable by the F in the name)

## Slide 4: PROFIsafe – the facts
Safety telegram is transmitted via separate safety module
We support the XP safety module (V2.6.1. expanded)
And also the obsolete LP Safety module (V2.4) (S7-300/400)
PROFIsafe can be combined with all Stöber DS6 applications
Safety functions SS1 and STO can be activated via PROFIsafe
Status feedback SS1_active and STO_active via PROFIsafe Safety
characteristics SIL3 / Ple (Cat. 4) (HW identical SY6)

## Slide 5: Adjust PROFIsafe adress
1. Activate safety in PLC
2. Check safety destination adress area (for slaves)
4. Choose safety destination adress
for every drive (slaves)
(Here 2 + 8 = 10)
Restart drive controller !
5. Set the same safety source adress for every drive in TIA
3. Check safety source adress (PLC)

## Slide 6: Adjust SS1 Time – DS6 and TIA Portal
1. Choose SS1 time in TIA Portal for the drive
2. Fill in SS1 time in DS6 assistant
3. Calculate F_iPar_CRC
and fill in TIA Portal
Important: The SS1-time is given in multiples of 10ms, so for example the value 100 corresponds to 100*10ms = 1s.

## Slide 7: Connecting Safety Binary Signals – naming tags
Diagnostic Bits STO / SS1
Input adress area
PROFIsafe Telegramm 30
Request Bits STO / SS1
Output adress area
1. define variable names for the safety functions STO and SS1

## Slide 8: Usage of safety I/O‘s in safety program
Diagnostic Bits STO / SS1
Input adress area
Request Bits STO / SS1
Output adress area

## Slide 9: Acknowledgement for reintegration
Find more information at siemens
Industry online support:

## Slide 10: Structure of Communication modules in HW Manager
Module
Submodule
Process Data Modules (since years)
M101–M107 all cons. 2W – 36W
(M111–M117 item cons. 2W – 36W)
Safety Modul (LP, obsolete)
Safety Module (XP)
PROFIDRIVE Modules
New
New
Telegram 1
Telegram 2
Telegram 3
Telegram 111
New
Choice depending on the lenght
Content changeable
Only available with Safety Device
Only available with Safety Device
Device
Single / DoubleAxis
Safety / No Safety
Defined content not changeable

## Slide 11: Possible Combinations in Hardwaremanager of Siemens
Devices
Modules and Submodules
PS: PROFISafe
PD1: PROFIdrive V1
(PD2 will include
Isochronous Real Time
functionality IRT)
The formerly known
Process data modules can be used
instead of PROFIdrive Module
PROFIdrive Module
Allows the usage of
Submodules Telegram1 to 111.
Safety Modules can only be used with PROFIsafe Devices (PS)

## Slide 12: Safety cycle time
cycletime safety program
independend of plc task
Independend of bus cycle

## Slide 13: Live Demo
Hardwaremanager / Possible Combinations
Naming of tags and usage in the safety program
Usage of status signals in the safety program
Reintegration safety program after safety error
If you have questions, please give me a feedback with the hand symbol.

## Slide 14: Thank you for your attention !

## Slide 15: Outlook to part II
You get the 5 PROFIdrive Examples for DriveLib (T1, T11)
and Technology Objekts (T1, T3, T11).
Please have a look and see more details in part II
in december 7th 2021.