## Slide 1: TC6 drive controller

## Slide 2: Sizes
Type | Size | Axis controller
TC6A062 | Size 0 | Double-axis controller
TC6A162 | Size 1 | Double-axis controller
TC6A261 | Size 2 | Single-axis controller

## Slide 3: TC6 Interface
Analog inputs and TTL encoder simulation

## Slide 4: TC6 for analog set value
IO interface for speed reference and encoder simulation
NO fieldbus interface
Safety function STO via terminal (SR6A)
  Certified for PLe (Cat. 4) and SIL 3
Control modes for
  Lean Motors LM
  Synchronous Servo Motors (e.g., series EZ)
  Asynchronous Motors (e.g., IE2 / IE3)

## Slide 5: IO interface TC6
TC6
Incremental
A / B / 0
Axis A
Signal A
Signal B
Signal 0
Incremental
A / B / 0
Axis B
Signal A
Signal B
Signal 0
Digital IO
Ready A
Ready B
DI1: Enable A
DI6: Enable B
DI2: Reset A
DI7: Reset B
Analog Inputs
Analog input A
Analog input B
IO interface
±10 V set value
  Resolution 12 Bit
TTL Encoder simulation as actual value
  Signals: A, B, Zero
  Maximum input frequency: 500 kHz
Digital outputs: ready
Digital inputs: enable and reset
Safety technology
Safety function STO via terminals (SR6A)

## Slide 6: X117