## Slide 1: OCS – One Cable Solution with EnDat 3 encoders
Confidential – For internal use only!

## Slide 2: Presentation OCS with HIPERFACE DSL 2016
Appeared in 2016 as the best technical solution

## Slide 3: Current status OCS with HIPERFACE DSL
Limited industrial reliability
  Problems with the transmission path from the encoder to the drive controller
    Partially from 15 m line length output choke required (+ 335 € gross price)
  Customer Progress
    Retrofitting of up to 20 output chokes in control cabinets
    Additional control cabinet for mounting the output chokes in the series
Limited reliability in some components
  Communication protocol of the HIPERFACE DSL encoders
    Requires min. 5 telegrams/cycles to restore the position
    Complex and unreliable calibration functions
    SICK Stegmann is testing with with „ancient“ drive controllers („ slow switching IGBT“)
    …
  Hybrid cables
    Required shielding of the DSL wires
    Towing capability (for use in drag chains)
    …

## Slide 4: OCS One Cable Solution
We now have the know how for OCS without chokes and drag chain up to 50m

## Slide 5: OCS – Components involved
SICK
HIPERFACE DSL®
Heidenhain
EnDat 3
<= 50 m
Encoder interface and protocol
  SICK HIPERFACE DSL® / Heidenhain EnDat 3
Hybrid cables
Interface of drive controllers (hardware & firmware)
Hybrid cable

## Slide 6: OCS – The prime example of a system solution
Result of the cooperation of an interdisciplinary STÖBER team consisting of MCGM, MCE, SPE, SPM with the manufacturers Heidenhain and Helukabel
  SYSTEM-solution!
Cooperation with Heidenhain on EZ synchronous servo motors and EnDat 3
  New encoder EQI1131-E30-R2 in two-wire technology
  Development and pre-series samples Heidenhain
  Coordination of circuit design between Heidenhain and STÖBER
  Test of sample drive controller with hybrid cable in Heidenhain drag chain system
Cooperation with Helukabel
  Essential design ideas from STÖBER
  Hybrid cable generation 2.1
  Improved internal shielding of the DSL wire pair
  Joint test of hybrid cable variants in 27 m drag chain test set-up

## Slide 7: OCS – technical constraints SI6/SC6
Encoder interface and protocol
  SICK HIPERFACE DSL®
  Heidenhain EnDat 3 (encoder available from Heidenhain since 2020-Q4)
EnDat 3.0 transceiver chip THVD1450
  Higher transmission frequency
  Better ESD behavior (higher robustness)
  Higher common mode tolerance, much better than EIA-485 standard (former RS-485)
  SC6/SI6 with Design 9 control section and DS6 V. 6.5-B available from 2021-Q1
Communication protocol
  EnDat 3 transmits position in each cycle, HIPERFACE DSL transmits acceleration values (5 cycles to get a new position)
  HIPERFACE DSL measures itself once on the cable (sensitive dependence)
  EnDat 3 resynchronizes with each telegram, robust against cable changes
SICK
HIPERFACE DSL®
Heidenhain
EnDat 3

## Slide 8: OCS – Cable development in cooperation with cable manufacturer
Hybrid cable
Target: Fault-free operation with up to 50 m cable length without choke in the drag chain
Generation 0 Cable with additional extrusion via DSL wire pair (SICK specification!)
Generation 1 Additional extrusion and double shielding DSL wire pair
Generation 2 Revised cable with new optimized shielding concept, improved crosstalk behavior and more stable properties in the drag chain
  Smallest permissible bending radius: Freely movable: 10 x dout
  Hybrid cable to be used with EnDat 3 and HIPERFACE DSL®
  Tests in house and in the cable manufacturer's drag chain
  Test with PROGRESS machine (Running since beginning of january 2021)
Development 2017 up to 2020!
U
V
DSL
Brake
PE
W
Shielding
Principle sketch Hybrid cable generation 2.1

## Slide 9: OCS – Validation of the hybrid cables under laboratory conditions
In 2019 test conditions much tougher and thus adapted to reality
  Market standard cable specifications do not fit "OCS/drag chain/50m reality".
Test of 50 m cable in the drag chain in operation with drive controller SC6A162 and synchronous servo motor EZ503U
Setup:

## Slide 10: Hybrid cable gen. 1 resistance change = measure for wear
First error after approx. 300.000 drag chain cycles
Chart: 
Chart: 
Widerstand in [Ω/km]
Cable gen. 1 were pure test cables, were not delivered to customers!
Steps of 100!
Overall shield
Resistance
Cycle number of cables

## Slide 11: Hybrid cable gen. 2.1 resistance change = measure for wear
Chart: Änderung Leiterwiderstände 29000594 bis 522000 Zyklen
| 10000 | 20000 | 30000 | 40000 | 50000 | 66831 | 76831 | 86831 | 96838 | 106838 | 116838 | 126838 | 136838 | 146838 | 156839 | 166839 | 176839 | 186839 | 196839 | 206839 | 216848 | 226848 | 236849 | 246849 | 256849 | 287778 | 297778 | 307782 | 317782 | 327782 | 337782 | 347782 | 357782 | 367782 | 377782 | 381939 | 391939 | 401939 | 411940 | 421940 | 431940 | 441940 | 451940 | 461940 | 471940 | 481941 | 491941 | 501941 | 511952
Gesamtschirm | 7.043 | 7.121 | 7.147 | 7.173 | 7.017 | 7.019 | 7.121 | 7.225 | 7.251 | 7.251 | 7.355 | 7.355 | 7.406 | 7.303 | 7.432 | 7.484 | 7.355 | 7.459 | 7.51 | 7.563 | 7.563 | 7.588 | 7.588 | 7.588 | 7.667 | 7.718 | 7.666 | 7.771 | 7.823 | 7.849 | 7.9 | 7.822 | 7.848 | 7.952 | 7.979 | 7.979 | 7.694 | 7.952 | 7.77 | 7.835 | 7.822 | 7.849 | 7.848 | 7.926 | 7.845 | 7.837 | 7.848 | 7.874 | 7.835 | 7.845
The aging of the overall screen could be significantly reduced. Target of 20 ohms/km not exceeded.
0.5 steps!
Overall shield
Change overall shielding resistance
Cycles over runtime
resistance

## Slide 12: OCS – new hybrid cables generation 2.1
Available new cables
  (4x1,5 + (2x0,75) + (2xAWG22)) with con.23
  (4x2,5 + (2x0,75) + (2xAWG22)) with con.23
STÖBER imprint on the cable
  Exclusivity
Technical framework for use in energy chains
  10 x D for multiple movements
  5 m/s2 up to 20 m distance
  5 mio. bending cycles
  4 m/s traversing speed
  Torsion max. +/-30°/m
Raw cable with cURus
Operation of motors up to size EZ705U_140 possible
Fig. Hybrid cable gen. 2.1 (4x2,5 + (2x0,75) + (2xAWG22))

## Slide 13: Connection method manual
Includes
Connection description
Technical Data
  Diameter
  Weights
  Capacitance / Inductance
Determining the cable code for ready-made cables in 3 steps
Ready-made hybrid cables
    List of ready-made cables (part numbers of the different lengths)
Accessories
  TEP output chokes

## Slide 14: OCS – measures drive controller
Changeover to new transceiver chip THVD1450
  Same transceiver chip as in the EQI1131-E30 EnDat 3 encoder
  Compatible with HIPERFACE DSL® (EKM36 / EDM35)
  SI6/SC6 Design 9 control parts
Introduction EnDat 3 with firmware V 6.5-B
  Available in parallel with HIPERFACE DSL®
HIPERFACE DSL axes can be replaced by EnDat 3 axes
  Encoders are detected automatically

## Slide 15: OCS – EZ servo motors with EQI1131-E30
OCS with EnDat 3
  EQI1131 – 12 Bit multiturn, 19 Bit singleturn
  PTC triplets or Pt1000 connectable and data transmission via EnDat 3 protocol
Field test at company Progress and other customers
  First machine of Progress running since January 4th, 2021, without any problems

## Slide 16: Current status
The STÖBER system OCS with EnDat 3
Drive Controller SI6/SC6
New hybride cable Gen. 2.1
EZ Servo motors with EQI1131 ???
  EZ301 … EZ705U_140
  EZ401B … EZ703B_122
  EZS501U … EZ703U_122
  EZS501B … EZS703M_122
Gear boxes