## Slide 1: Advantages of High Speed Motors
J. Kübler, PMT March 2022 – Task from PMT November 2021

## Slide 2: Statistics Synchronous Servomotors
 | 2019 | 2020 | 2021 | 2022 | Summe
EZ ≤ 3000rpm | 9933 | 8181 | 11015 | 3251 | 32380
EZ > 3000rpm | 3480 | 3016 | 4487 | 1305 | 12288
Summe | 13413 | 11197 | 15502 | 4556 | 44668
Anteil ≤ 3000rpm | 74% | 73% | 71% | 71% | 72%
Chart: Baureihe EZ
| 2019 | 2020 | 2021 | 2022 | Summe
EZ ≤ 3000rpm | 9933 | 8181 | 11015 | 3251 | 32380
EZ > 3000rpm | 3480 | 3016 | 4487 | 1305 | 12288
Summe | 13413 | 11197 | 15502 | 4556 | 44668
Anteil ≤ 3000rpm | 0.74055 | 0.73064 | 0.71055 | 0.71356 | 0.7249
 | 2019 | 2020 | 2021 | 2022 | Summe
ED/EK ≤ 3000rpm | 3625 | 2851 | 3219 | 853 | 10548
ED/EK > 3000rpm | 3546 | 2552 | 3432 | 845 | 10375
Summe | 7171 | 5403 | 6651 | 1698 | 20923
Anteil ≤ 3000rpm | 51% | 53% | 48% | 50% | 50%
Chart: Baureihe ED/EK
| 2019 | 2020 | 2021 | 2022 | Summe
ED/EK ≤ 3000rpm | 3625 | 2851 | 3219 | 853 | 10548
ED/EK > 3000rpm | 3546 | 2552 | 3432 | 845 | 10375
Summe | 7171 | 5403 | 6651 | 1698 | 20923
Anteil ≤ 3000rpm | 0.50551 | 0.52767 | 0.48399 | 0.50236 | 0.50413
EZ Motoren sind sehr hochpolig, dadurch entstehen hohe Blindströme. Dies kann zum Baugrößensprung beim Antriebsregler führen.
Für hohe Drehzahlen sind hohe Frequenzen erforderlich (>600Hz) Viele Antriebsregler sind wegen der „Dual Use“ Verordnung auf 599Hz begrenzt.
EZ motors have very high polarity, which results in high reactive currents. This can lead to a step change in the size of the drive controller.
For high speeds, high frequencies are required (>600Hz) Many drive controllers are limited to 599Hz because of the "Dual Use" regulation.

## Slide 3: AMADA LCG
X-Axis (Gantry) Rack and Pinion
Mass: 650kg  2/3 on one side m=433kg
a = 10 m/s² v = 2 m/s
Possible Solution: ZV330S PH732SXSR0160 EZ505B/6000 (n1N=6000 1/min currently not available)
Current Solution:
ZV330S PH731SXSR0070ME
Fanuc alpha22-4000i
IM=2,8
IM=2,9
although geared motor
no coupling
Ltot=161+215=376mm □Mot=174mm
mtot=12+29=41kg
Ltot=436mm (FC 86mm)
□Mot=115/135
mtot=26kg

## Slide 4: Mecanumeric
X-Axis (Gantry) Rack and Pinion
Mass: 600kg  1/2 on one side m=300kg
a = 2 m/s² v = 1,33 m/s
Possible Solution: ZV216SE P331_0040 EZ401U/3000
Current Solution:
ZV216SE P331_0080 EZ302U/6000
IM=9,5
IM=26,5
Ltot=68,5+112=180,5mm
□Mot=72mm
mtot=3,6kg
Ltot=65+98=163mm
□Mot=98mm
mtot=5,5kg
1142,-€
1341,-€

## Slide 5: Mecanumeric
Y-Axis Rack and Pinion
Mass: 200kg
a = 2 m/s² v = 1,33 m/s
Possible Solution: ZV216SE P331_0040 EZ401U/3000
Current Solution:
ZV216SE P331_0080 EZ302U/6000
IM=4,3
IM=13,6
Ltot=68,5+112=180,5mm
□Mot=72mm
mtot=3,6kg
Ltot=65+98=163mm
□Mot=98mm
mtot=5,5kg
1142,-€
1341,-€

## Slide 6: RODIN4D
Rotary Table
Inertia: 0,8kgm²
α = 70 rad/s² n2 = 167 1/min
Possible Solution: PH432_0400 EZ302U/6000
Current Solution:
PH432_0250 EZ401U/3000
IM=12,4
IM=12,2
Problem at gearbox:
The allowed n2N drops down
from 180 to 125 1/min due to a to small increase of n1N from 4000 1/min (i=25) to 4500 1/min (i=40).
i=40 should have n1N=6000 1/min
Ltot=223,5mm
□Mot=98mm
mtot=8,2kg
Ltot=241mm
□Mot=72mm
mtot=6,3kg
2050,-€
1951,-€

## Slide 7: Thomas Construction
Y-Axis Pulley Belt
Mass: 61kg
a = 2 m/s² v= 1 m/s
Possible Solution: PE422_0250EZ301U/6000
Current Solution:
PE421_0100EZ402U/3000
IM=7,3
IM=7,2
Ltot=258mm
□Mot=98mm
mtot=7,9kg
Ltot=265mm
□Mot=72mm
mtot=5,5kg
995,-€
1014,-€

## Slide 8: Thomas Construction
Z-Axis Pulley Belt
Mass: 52kg
a = 2,7 m/s² v= 1,1 m/s
Possible Solution: PE522_0250EZ401U/6000
Current Solution:
PE521_0100EZ502U/3000
IM=3,5
IM=2,6
Problem at gearbox:
The allowed n2N drops down
from 300 to 135 1/min due to a to small increase of n1N from 3000 1/min (i=10) to 3400 1/min (i=25).
i=25 should have n1N=7500 1/min
Ltot=298mm
□Mot=115mm
mtot=12kg
Ltot=320mm
□Mot=98mm
mtot=12kg
1246,-€
1308,-€

## Slide 9: Krauss Maffei
Rotary Table G100 WPL350
Inertia: 40kgm²
α = 30/-45 °/s² n2 = 12 1/min
Possible Solution: K813_0360 EZ803B/4500
Current Solution:
K813_0230 EZ805B/2000
IM=63
IM=40
Ltot=839mm
□Mot=190/215mm
mtot=198kg
Ltot=757mm
□Mot=190/215mm
mtot=184kg
6486,-€
5792,-€
Motor with winding for 4500rpm is currently not avalilable. Roughly estimated this could be the voltage lim curve.

## Slide 10: Krauss Maffei
Rotary Table G100 WPL260
Inertia: 36kgm²
α = 51/-64 °/s² n2 = 10,5 1/min
Possible Solution: K813_0360 EZ803U/4500
Current Solution:
K813_0230 EZ805B/2000
IM=57
IM=29
Ltot=839mm
□Mot=190/215mm
mtot=198kg
Ltot=667mm
□Mot=190/215mm
mtot=177kg
6486,-€
5474,-€
Motor with winding for 4500rpm is currently not avalilable. Roughly estimated this could be the voltage lim curve.

## Slide 11: Krauss Maffei
Rotary Table G50 WPL260
Inertia: 21kgm²
α = 51/-64 °/s² n2 = 10,5 1/min
Possible Solution: K813_0360 EZ803U/4500
Current Solution:
K813_0230 EZ805B/2000
IM=33
IM=17
Ltot=839mm
□Mot=190/215mm
mtot=198kg
Ltot=667mm
□Mot=190/215mm
mtot=177kg
6486,-€
5474,-€
Motor with winding for 4500rpm is currently not avalilable. Roughly estimated this could be the voltage lim curve.

## Slide 12: Rudholzer
Z-Axis: Ball Screw p=32mm/U
Mass: 150kg
a = 10 / - 15m/s² v= 0,54 m/s
Possible Solution: K102_0060 EZ502U/6000
Current Solution:
K202_0040 EZ703U/4500
IM=0,12
IM=0,2
Gearbox max input speed is limited to 5000rpm.
Needed: 6000rpm
Motor runs in field weekening
Ltot=389mm
□Mot=145mm
mtot=30kg
Ltot=325mm
□Mot=115mm
mtot=16kg
1946,-€
1405,-€

## Slide 13: Rudholzer
Door Lift: Ball Screw p=100mm/U
Mass: 50kg
a = 0,5m/s² v= 0,5 m/s
Possible Solution: KL102_0160 ED212U/6000
Current Solution:
K102_0140 EZ303U/3000
IM=0,3
IM=0,28
Ltot=342mm
□Mot=72mm
mtot=12kg
Ltot=265mm
□Mot=55mm
mtot=6,5kg
1135,-€
1167,-€

## Slide 14: P.W. Lenzen
Continous Duty S1
M2=267Nm at n2=150 1/min
Possible Solution: P732_S0400 EZ702U/6000
Current Solution:
P732_S0200 EZ703U/3000
IM=0,0
IM=0,0
Ltot=415,5mm
□Mot=145mm
mtot=26kg
Ltot=390,5mm
□Mot=145mm
mtot=24kg
1273,-€
1118,-€
Gearbox nominal input speed is limited to 3700rpm.
Needed: 5250rpm

## Slide 15: Zarian
Z-Axis: Rack and Pinion
Mass: 2000kg
a=2,5m/s² v=0,65m/s
Possible Solution: K713_0500 EZ802U/4500
Current Solution:
K713_0390 ED806U/3000
IM=0,74
IM=0,76
Ltot=742,5mm
□Mot=190mm
mtot=140kg
Ltot=581,5mm
□Mot=190mm
mtot=118kg
5535,-€
4042,-€
Capture K713 with 4500rpm motors is missing in Catalog and ServoSoft.
Even though the motor is existing and the gearbox allows this speed.

## Slide 16: Length Comparison
 | Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Total Length LS | 376 | 163 | 163 | 223,5 | 258 | 298 | 839 | 839 | 839 | 389 | 342 | 415,5 | 742,5 | 
Total Lenght HS | 350 | 180,5 | 180,5 | 241 | 265 | 320 | 757 | 667 | 667 | 325 | 265 | 390,5 | 581,5 | 
Length Delta HS in % | -7% | 11% | 11% | 8% | 3% | 7% | -10% | -21% | -21% | -16% | -23% | -6% | -22% | -7%
Chart: Length Comparison
| Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Total Length LS | 376 | 163 | 163 | 223.5 | 258 | 298 | 839 | 839 | 839 | 389 | 342 | 415.5 | 742.5
Total Lenght HS | 350 | 180.5 | 180.5 | 241 | 265 | 320 | 757 | 667 | 667 | 325 | 265 | 390.5 | 581.5
Length Delta HS in % | -0.069149 | 0.10736 | 0.10736 | 0.0783 | 0.027132 | 0.073826 | -0.097735 | -0.20501 | -0.20501 | -0.16452 | -0.22515 | -0.060168 | -0.21684 | -0.065353
The High Speed solution is in average 7% shorter than the Low Speed solution!

## Slide 17: Weight Comparison
The High Speed solution has in average 23% less weight than the Low Speed solution!
 | Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Weight LS | 41 | 5,5 | 5,5 | 8,2 | 7,9 | 12 | 198 | 198 | 198 | 30 | 12 | 26 | 140 | 
Weight HS | 26 | 3,6 | 3,6 | 6,3 | 5,5 | 12 | 184 | 177 | 177 | 16 | 6,5 | 24 | 118 | 
Weight Delta HS in % | -37% | -35% | -35% | -23% | -30% | 0% | -7% | -11% | -11% | -47% | -46% | -8% | -16% | -23%
Chart: Weight Comparison
| Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Weight LS | 41 | 5.5 | 5.5 | 8.2 | 7.9 | 12 | 198 | 198 | 198 | 30 | 12 | 26 | 140
Weight HS | 26 | 3.6 | 3.6 | 6.3 | 5.5 | 12 | 184 | 177 | 177 | 16 | 6.5 | 24 | 118
Weight Delta HS in % | -0.36585 | -0.34545 | -0.34545 | -0.23171 | -0.3038 | 0 | -0.070707 | -0.10606 | -0.10606 | -0.46667 | -0.45833 | -0.076923 | -0.15714 | -0.2334

## Slide 18: Inertia Missmatch Comparison
The High Speed solution has in average a 18% lower (better) Inertia Missmatch than the Low Speed solution!
 | Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Inertia Missmatch LS | 2,8 | 26,5 | 13,6 | 12,4 | 7,3 | 3,5 | 63 | 57 | 33 | 0,12 | 0,3 | 0 | 0,74 | 
Inertia Missmatch HS | 2,9 | 9,5 | 4,3 | 12,2 | 7,2 | 2,6 | 40 | 29 | 17 | 0,2 | 0,28 | 0 | 0,76 | 
IM Delta HS in % | 4% | -64% | -68% | -2% | -1% | -26% | -37% | -49% | -48% | 67% | -7% | 0% | 3% | -18%
Chart: Inertia Missmatch Comparison
| Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Inertia Missmatch LS | 2.8 | 26.5 | 13.6 | 12.4 | 7.3 | 3.5 | 63 | 57 | 33 | 0.12 | 0.3 | 0 | 0.74
Inertia Missmatch HS | 2.9 | 9.5 | 4.3 | 12.2 | 7.2 | 2.6 | 40 | 29 | 17 | 0.2 | 0.28 | 0 | 0.76
IM Delta HS in % | 0.035714 | -0.64151 | -0.68382 | -0.016129 | -0.013699 | -0.25714 | -0.36508 | -0.49123 | -0.48485 | 0.66667 | -0.066667 | 0 | 0.027027 | -0.17621

## Slide 19: Gross Price Comparison
The High Speed solution is in average 10% cheaper than the Low Speed solution!
 | Amada | Mecanumeric X | Mecanumeric Y | Rodin4D | Th. Construction Y | Th. Construction Y | Krauss Maffei G100 WPL350 | Krauss Maffei G100 WPL260 | Krauss Maffei G50 WPL260 | Rudholzer Z | Rudholzer Door Lift | P.W.Lenzen | Zarian | Average
Gross Price LS |  | 1341 | 1341 | 2050 | 995 | 1246 | 6486 | 6486 | 6486 | 1946 | 1135 | 1273 | 5535 | 
Gross Price HS |  | 1142 | 1142 | 1951 | 1014 | 1308 | 5792 | 5474 | 5474 | 1405 | 1167 | 1118 | 4042 | 
Gross Price Delta HS in % | 0% | -15% | -15% | 5% | 2% | 5% | -11% | -16% | -16% | -28% | 3% | -12% | -27% | -10%

## Slide 20: Technical Disadvantages of Higher Speeds
Temperatur level is increasing
With higher temperatur increases the internal pressure  faster seal wear out.
With higher temperatur the lifetime of the oil is shorter
Running noise level is increasing

## Slide 21: A Point to think about
A High Speed Solution needs higher ratios.
At the P / PH and PE line this leads very often to a 2-stage gearbox
The 2-stage gearboxes are about 60 – 80% more expensive.
This is overcompensating the price advantage of the smaller motor.
Is it possible to resuce the 2-stage prices to about +30 – 50%?
Try to use K, C or F-gearboxes, because higher ratios are here for free!