## Slide 1: Lean motor Start-up
Experiences from field applications
Technical meeting 2022 Lutz Augenstein

## Slide 2: Experiences from field applications
Belt driven transport systems are always a simple application, isn't it?
Presentation of two “simple” applications
  Realized with Lean motor…
  …which were not so simple applications as expected

## Slide 3: Application sealing machine
Sealing of glasses
Existing customer (not system)
So far solved by
  IE2 ASM geared motor, sensorless
  Danfoss inverter
  Asynchron motor solution
Requirements
  „Smoothness run“
  No IE3 ASM (size)
    „IE5“
  Medium number of machines
    1 parameter setting for all types

## Slide 4: Application sealing machine
Danfoss -> SC6x62
IE2 ASM motor -> LM motor
Test machine was built
  Good results
First machines delivered to end customer
  No problems…
  … but after some months
Jerking of the products on the belt at a new machine
End customer with low viscosity product
And at „some machines“ in the field
Jerking of the belts get noticed

## Slide 5: Application sealing machine – jerking at water tests

## Slide 6: Application sealing machine – front view
v1
x
x
Lean
Side belt
v2=v1+x
Lean
Glasses
Caps

## Slide 7: Application sealing machine – diagnostic
Intermittent mechanical coupling
  Both axis in speed control
    Jog function still in position control
  Different velocitys
    Creates the screwing of the cup
    “axis” also work against each other (or the spring force?)
Products with different viscosity
v1
x
v2=v1+x

## Slide 8: Application sealing machine – diagnostic
x
x
x
x
x
x
x
x
x
x
x
Sealing
Belt from other machine distance ~5m (belt length >10m)
1. Stand alone machine
2. Classical construction
Sealing
Sealing
Customer, filler
Customer, filler
3. New construction
Glide rail
Lubrication

## Slide 9: Application sealing machine – variation belt return

## Slide 10: Application sealing machine – actions
Lean Velocity control without integration
  C32 = 0
  Try to „emulate“ ASM U/f control
    Lean has always closed loop control
  Try to reduce overshot reaction
    After glas leaves the sealing and belt moves „free“
EZ Standard velocity control

## Slide 11: Application sealing machine – actions Lean
With integration
Belt get slowed down during glas contact
Overshots if glas leaved the sealing
Needs time to calm down
Without integration
Belt get slowed down during glas contact
Needs time to reach v again (C31 dependend)

## Slide 12: Application sealing machine –Lean vs EZ
Lean with integration
Lean without integration
EZ
20 rpm/decade

## Slide 13: Application sealing machine - conclusion
It was an asynchronous machine application in the past
  And the ASM open loop control had advantages for the application
  Just like the higher mass of inertia with ASM
  We were “good enough” with Lean after optimisations
Customer decided for servo for the transportation belt
  He want the best performance for belt that is possible
  Sealing belt stays Lean
We delivered parts and now the whole system
  We replaced Danfoss
  Price of complete solution is similar then before
v1
x
x
Lean
Side belt
v2=v1+x
Lean
Glasses
Caps

## Slide 14: Application bottle inspector
Inspection of empty bottles/glasses before filling
Existing system customer
So far solved by
  MDS 5000, MC_GearIn
  ED geared motor
  Servo motor solution
Requirements
  Following error < 1 mm
  High number of machines
    1 parameter setting for all types
  Cheaper solution than before

## Slide 15: Application bottle inspector – new solution
MDS 5000 -> SC6x62 + SI6x61
MC_GearIn
ED motor -> LM motor
Test machine was built
  Good results
First machines delivered to end customer
  No problems…
  … but after some months
Problems on „some machines“ in the field
Control instability
  Error events; encoder failure 37 (2: max velocity) etc.
Test machine: little jerking of the transport belt from time to time

## Slide 16: Application bottle inspector – top view
x
x
x
x
Lean side belts
Lean side belts
Lean horizontal belt
Motor from other machine horizontal belt
External Encoder
for Master-Slave
v1
v1 (Master)
v2 (Master+x)
v2
Inspector
Bottles

## Slide 17: Application bottle inspector – diagnostic
Intermittent mechanical coupling
  Both axis in position control
  Different velocitys
    “Slip” creates the rotation of the bottle
    But the axis also work against each other
Different length and height of belt
  Aging of belt
x
x
x
x
v1 (Master)
v2 (Master+x)
mechanical coupling

## Slide 18: Application bottle inspector – diagnostic
Conflict in finding a solution
  Reduce effect of less position/master encoder quality to control by using Master-Slave “speed coupling”
    Following error will increase
  Making the axis “stronger” (slip should create only rotation) by higher proportional gain
    But stability limit for Lean is less than for servo (due to encoder)
  Increase robustness by reducing the control (Kp)
    Following error will increase
  Reduce reaction to mechanical coupling by deactivating integration part of control
    Following error will increase
  Increase stability limit by “improve of the encoder” ???
    Application specific

## Slide 19: Application bottle inspector - “improve of the encoder”
The customer needs a temporary solution for delivered machines
For series machine he will go back to servo
Only one last chance, „Lean Expert mode“
Try to adjust the speed observer
Change B100 from LM type to „user definied“
Increase position/velocity controller till stability limit is reached
Set B138[0] to a smaller or higher value
Try if this increase stability limit; keep the best B138[0]
Repeat with B138[1] and [2]

## Slide 20: Application bottle inspector - conclusion
It was a servo application in the past and it will one again
  We were close with Lean
Customer has higher requirements („1mm“) than a simple belt application
  And he tested in the beginning with success
We delivered the whole system and will continue to do
  We changed from MDS and ED to actual SC6/SI6 and EZ
  Electronic part of solution is now cheaper for customer
x
x
x
x
Lean side belts
Lean side belts
Lean horizontal belt
Motor from other machine horizontal belt
External Encoder
for Master-Slave
v1
v1 (Master)
v2 (Master+x)
v2
Inspector
Bottles