## Slide 1: Software NEWS
What’s new since the last technical meeting October 2019?
Technical meeting 2021 Lutz Augenstein

## Slide 2: Agenda
Overview 6.4-E > 6.5-B
Important and highlights 6.5-D/6.5-E
Electronic nameplate
Outlook

## Slide 3: Timeline versions
6.4-D
Meeting 2019
6.4-E
2020
  6.4-F
6.5-A
2020
6.5-B
2020
  6.5-C
6.5-D
2021
  6.5-E
  Meeting 2021
Function release
Service pack release
Version history
Document ID 443240

## Slide 4: Overview 6.4-E (spring 2020)
>150 improvements, for example
Switching the firmware fieldbus variant: EtherCAT <> PROFINET (SC6, SI6)
EtherCAT: Cycle times 250 μs and 500 μs (SC6, SI6)
New import functions
Graphical programming: User adjustments area
Old „style“
New „style“

## Slide 5: Overview 6.5-A (summer 2020)
>150 improvements
One Cable Solutions with an EnDat 3 encoder (SC6, SI6)
Improved Suite performance
  Load, save, import, copy
Shortened click paths
  Update project configurations, clean up project or manage scope images
6.5-D

## Slide 6: Overview 6.5-B (autumn 2020)
>90 improvements
Get there faster
  Quick change between the different suite areas
Scope: Direct image

## Slide 7: Important topic and highlights 6.5-D/-E (summer 2021)
>90 improvements
Use SDO Info service for EtherCAT and changed addressing of array and record parameters in standard
Using the drive controller comparison, you get a quick overview of your projects
Optimize your control cascade with the new user interface for the set value generator
Use the STO and SS1 safety functions via PROFIsafe as well as PROFIdrive type (SC6, SI6)
In Drive Based Synchronous type applications, the electronic cam disk is also available for synchronous operation in addition to the electronic gear unit

## Slide 8: What is SDO Info?
SDO Info Service enables the EtherCAT controller to
  Read out all objects defined in the object dictionary from the drive controller
    Including object properties (data type, write/read access, rights, mapping capability)
Could use for
  Easy add parameters to startup list
  Get „data“ for programming SDO communication
  Diagnostic during startup
  Set values during startup

## Slide 9: Requirements
Firmware 6.5-D or higher
Rx device control of type „SDO Info“
  Our new default
New ESI device description for EtherCAT controller

## Slide 10: Settings for SDO Info
A268 defines the amount of parameters
  Only EtherCAT objects; only STÖBER parameters; combination
  Readout time 5s – 75s per drive controller
A213[1] has to be „raw values“, to get actual values
A12 defines the language of names
A10[2] access level

## Slide 11: Settings for SDO Info
Activate Online Dictionary in EtherCAT controller

## Slide 12: This is what SDO Info active looks like

## Slide 13: SDO Info – major change of addressing
For SDO info and for the mandatory compatibility to the standard EtherCAT, for the future
  We have to change the SDO address, only for none-CiA-402 (=STÖBER) parameters of type array and record
Generation 5 and 6 with none SDO Info Rx:
  Subindex 0 hex address the first array or structure element, Subindex 1 hex the second…
  Example E52 Information drive controller:
    Subindex 0 = E52[0] (Type of drive, e.g. SD6)
    Subindex 2 = E52[3] (Firmware version, e.g. 6.5-A)
Generation 6 with SDO Info Rx:
  Subindex 0 hex shows the highest available subindex, Subindex 1 hex address the first array or structure element…
  Example E52 Information drive controller:
    Subindex 0 = 8 (Size of array)
    Subindex 2 = E52[2] (production number, e.g. 800001)

## Slide 14: How can an EtherCAT controller differ with/without SDO Info?
SD6: Not at all
SC6, SI6 with ESI created with DriveControlSuite 6.5-C or older: Not at all
SC6, SI6 with ESI created with DriveControlSuite 6.5-D or higher: Yes, new revsion number
  EC Standard, Rev. Nummer 6100 (17D4 hex)
  EC SDO Info, Rev. Nummer 6500 (1964 hex)

## Slide 15: What happens if you mix SDO Info?
Don‘t mix

## Slide 16: What happens if you mix SDO Info?
New ESI with revision number (SC6, SI6)

## Slide 17: What happens if you mix SDO Info?
Old ESI or SD6, but new Rx in the drive controller
  PDO cyclic communication will work
  SDO with CiA 402 parameters will work
  Configure PDO mapping via SDO will work
  SDO access to Stöber standard parameters will work
  SDO access to Stöber array and record parameters will not work
    Data salad

## Slide 18: Drive controller comparison
Compare before establish online connection
  Comparison only between drives of the same „series“
  Find this function in the Online functions dialog

## Slide 19: Drive controller comparison
Checkbox inactive = Yellow highlight of differences

## Slide 20: Drive controller comparison

## Slide 21: Drive controller comparison
Compare drives in the project or external project file
  Comparison also between drives of the different „series“
  Find this function in the project tree context menue

## Slide 22: Set value generator
Remember Technical Meeting 2019?
  Optimization control cascade with control panel and scope
Another way to optimize velocity controller
  Find this function at the scope direct image view
Activation set value generator
Control panel - Activate, Enable, Reset
Set value for generator - D93, D94, D95
Optional - Variable parameter list integrated
motor type dependent
encoder dependent
load-dependent
0
1
2+3
4+5
load-dependent

## Slide 23: Set value generator
3. Shot a scope image
2. Use value generator
1. Set velocity controller
Optional - Safe image

## Slide 24: What is an electronic cam disc?
An electronic cam disc is a functionality in which
  a drive (slave) follows a master axis (master) synchronous with his position to the master position and
  the target position of the drive is not linear (no fixed x-to-y ratio) but is calculated from an x-to-y table from the actual position of the master axis.
The term cam disc or cam gear originates from the original mechanical solution of the motion task mentioned above.
  There, the "coupling" of master takes place via a disk rotated by the master, whose disk contour is transferred into a slave movement

## Slide 25: Representation of the cam plate in the motion diagram
360°
1. cycle
Master
50 mm
Slave
2. cycle
Master
50 mm

## Slide 26: Highlights cam disk
Ready to use
  Integrated in standard application Drive Based Synchronous
  Direct usable in command mode and motion block mode
    Standard function
    Parameterize it
    No programming

## Slide 27: Highlights cam disk
Cam designer integrated
  Interactive
  Free of license fees

## Slide 28: Highlights cam disk
Coupling command: MC_CamInAbsolute
Start of a preset cam plate
  The position from which the coupling should be active, i.e. from when the slave should follow the master synchronously, is explicitly specified by the user.
  The motion profile for the compensation of the slave / master actual position and the synchronous position is calculated automatically from the differences of the positions.
    The profile uses jerk-limiting mathematics, the jerk results indirectly
    Identical to MC_GearInPosition
  Master and slave can be interpreted relative or absolute
    With absolute the coupling point must be on the curve

## Slide 29: Highlights cam disk
Sequencing of cams
  Parameterize it
Single shot cam
Periodic cam
Sequence of cam

## Slide 30: Highlights cam disk
Cam design data „loss protection“
  Seperate storage of „design and execution data“
  Storage of „design data“ in the drive controller
Project file
Drive controller 1
Cam disc 1
Cam disc 16
Movment points
design data
Reference points
execution data
Drive controller
x
Cam disc 1
Cam disc 16
Movment points
design data
Reference points
execution data
Drive controller 1
Cam disc 1
Cam disc 16
Movment points
design data
Reference points
execution data
Empty DS6

## Slide 31: Availability cam disk
Software
  DriveControlSuite, Firmware, Application
  Version 6.5-D
  Released August 2021
  For all generation 6 drive controller: SD6, SC6, SI6
Documentation
  Parameter description German
  Manuals, en-fr parameter description
Project („Sales“) release
  Will take place when documentation is complete

## Slide 32: Do you remember electronic nameplate?
Since year 2000
  Motor settings
  Motor brake settings
  Current controller settings

## Slide 33: Gear unit data
2019 Gear unit data version 1
  Firmware 6.4-A, motor manufactured since september
  Geared motor data
  Motor adapter
    2nd brake settings
  Automatically set limitations
  Automatically set axis model
2020 Gear unit data version 2
  Firmware 6.5-A, motor manufactured since march
  Set axis model only on demand (Action B30)

## Slide 34: Gear unit data
Easier commissioning
  Data available electronically for DS6 and control system
  Automatic presetting of limitations and 2nd brake

## Slide 35: Gear unit data
Compliance with gearbox (nominal) data

## Slide 36: Outlook 6.5-F
Planned improvements: ~60
Planned completion: 12/2021
Main focus: grapical programming
Possibly: predictive maintenance, model based approach level 1