## Slide 1: System cables
Power, encoder and hybrid cables

## Slide 2: STÖBER system
Why will we secure the future of our company with the STOBER system?
Our path to a successful, stable future is based primarily on our technological expertise: Complete drive axis consisting of gear units, motors, cables and drive controllers – modular in design and freely scalable for precisely fitting, compact machine concepts – and compatible with market standards in the field of controls. A complete package with excellent service from a single supplier.

## Slide 3: STÖBER product portfolio
Control level
Field level
Actuator level
Drive controller
SD6, SC6, SI6
Geared motors

## Slide 4: STÖBER cable types
Encoder cable
Power cable
OCS hybrid cable

## Slide 5: Technique – insulation material
PVC
PP

## Slide 6: Insulation materials – PVC
Polyvinyl chloride
Operating temperature: -20° C to 105° C
General Properties:
  Good flexibility,
  Easy to dye, also translucent to transparent,
  Moderate weather resistance,
  Containing halogen
Examples of use:
  Switching wires and stranded wires, hose cables, low frequency cables, power control cables, flat ribbon cables, sheath for RG high frequency cables, data transmission cables, automotive and ignition cables
Comments: Halogenated, cheapest plastic, high dielectric constant εR (4-8)
PVC burns with a yellow, strongly sooty flame and quickly extinguishes without further external flaming
However, fires of PVC plastics produce hydrogen chloride, dioxins and also aromatics
We do NOT use!

## Slide 7: Insulation materials – TPE-E
Thermoplastic polyester elastomer
Operating temperature: -70° C up to 115° C
General Properties:
  Resistant to solvents and hydraulic fluids
  Halogen free
  Weather resistant, very good cold behavior
  Dielectric constant εR (3,3)
Examples of use:
  Thin core insulation for NF, vehicle and drag chain cables
  Outer insulation for helical cables

## Slide 8: Insulation materials – TPE-U (PUR)
Thermoplastic Polyurethane elastomer
Operating temperature: -60° C up to 80° C
General Properties
  High cold flexibility, good cut resistance
  High damping capacity
  Partly halogen free
  Weather resistant
  Dielectric constant εR (8)
Examples of use
  Hose cables, power cables
  Outer insulation for special cables for high mechanical and chemical requirements
Previous power and encoder cable

## Slide 9: Insulation materials – PP
Polypropylene
Operating temperature: -40° C to 100° C
General Properties:
  UV resistant due to appropriate stabilization
  Less stress cracking than PE
  A little stiff
  Halogen free
  High dielectric strength of up to 100 kV/mm
  Dielectric constant εR (2,5)
Examples of use
  Heating cables, special cables and data cables
Comments
  Polypropylene is one of the flammable plastics. PP continues to drip and burn without sooting after removal of the flame
  The combustion of PP primarily produces carbon dioxide, carbon monoxide and water.
New power and encoder cables

## Slide 10: Technique – Power cables: cross sections and current
4 power wires (1 (U), 2 (V), 3 (W), PE)
2 brake wires (5, 6)
2 Thermal sensor wires (7, 8)
  PTC triplet
  Pt1000

## Slide 11: Technique – Structure encoder cable
5050044 (formerly 49484)
(3 x 2 x 0,14 mm² + 2 x 0,25 mm²)
44206
(3 × (2 × 0,14 mm²) + (2 × 0,25 mm²)) Twisted pairs, shielded and jacketed
44207
(2 x 2 x 0,25 mm² + 2 x 2 x 0,14 mm² + 2 x (2 x 0,14 mm²) + 2 x 0,34 mm²) Sinus and cosinus: twisted pairs, shielded and jacketed

## Slide 12: Technique – twisted pairs
Reduction of interference from external electromagnetic fields, as they act on the cable in constantly changing spatial directions due to the twisting and cancel each other out
Lower interference radiation of the cable itself
Reduction of crosstalk
Influence on the towing capacity due to the mechanical load
Data +
Data -
Clock +
Clock -
U2
0V GND
U2 Sense
Sketch encoder cable 5050044 (49484) EnDat 2.1 / 2.2 digital

## Slide 13: Technique – Shielding/1
Braided shield
Covering wires
Shielding foil

## Slide 14: Shielding /2
Braided shield (used with STÖBER system cables)
  The coverage of the inner conductors usually ranges between 85% and 90%, in special applications up to 98% coverage is possible (braid angle).
  Shield wire bundles usually consist of three to ten individual wires
  Shield is braided from bare or tinned copper wires, tinned version has better properties against corrosion
  Drag chain suitable, but can form gaps over time
  Advantages:
    Very good damping/attenuation (55-65 dB)
    Good mechanical properties (well suited for drag chains)
  Disadvantages
    Very slow and laborious processing (m/min)
    expensive
Fig. shield with wire bundles of 8 single wires

## Slide 15: Shielding /3
Shielding by covering wires
  Coverage of the inner conductors is usually between 95 and 100%
  Double covering wires shield with opposite stranding directions compensate disadvantages at high bending loads
  Shield made of bare or tinned copper wires is placed over inner conductor, tinned version has better properties against corrosion
  Very good torsional strength
  Advantages
    Easy processing, as the screen does not have to be "unbraided”
    Cheaper to manufacture due to simple process
    Faster processing than braiding (m/min)
  Disadvantages
    Poor mechanical properties (not suitable for cables in drag chain)
    Worse damping ( 30-40 dB)

## Slide 16: Shielding /4
Shielding foil
  Individual or all cores are wrapped with aluminum-laminated plastic foil (Winding angle)
  The coverage of the inner wires is usually 100%.
  Good shielding properties in the high frequency range
  Aluminum coated foil (coated outside, inside blank), coating used as a mechanical stabilizer
  Advantages
    Very good damping ( 60-65 dB)
    Fast process (m/min)
    Very cheap EMC protection
  Disadvantages
    Poor mechanical properties (not suitable for cables in drag chain)
    Foil breaks quickly
    Low effect at low frequencies

## Slide 17: DESINA cable colors
Shielded power cables: servo controller, frequency inverter, etc. Orange RAL 2003
Shielded encoder cables: Linear and rotary encoder, analog sensors Green RAL 6018
Fieldbus / hybride cables violet RAL 4001
Power cables unshielded: Device feed, three-phase motors Black RAL 9005
Control cables: 24 V power supply Grey RAL 7040
DESINA stands for DEcentralized and Standardized INstAllation Technology for Machine Tools and Production Systems
Goal: Standardization of the electrical, hydraulic and pneumatic installation of automated machine tools and production systems
  ISO 23570

## Slide 18: Electrical properties: cable capacitance and leakage currents
Leakage currents due to parasitic capacitances
Motor cable with grounded shield acts like a capacitor
High-frequency currents flow to ground via this capacitance!
M
3~
IShield
Drive Controller
Power Cable
Motor
Motor current

## Slide 19: STOBER encoder cables: 5 interfaces – 3 cable types
Interfaces
  Inkremental encoders HTL /TTL
  SSI encoders
  Sin-cos encoder
  EnDat 2.1 / 2.2 digital encoders
  Resolvers
  EnDat 2.1 sin-cos encoder
5050044: Overall shield,
Twisted pairs
44206: Overall shield,
Twisted, shielded and jacketed pairs
44207: Overall shield,
twisted, shielded and jacketed pairs for sin-cos signals,
Twisted pairs for EnDat and supply voltage

## Slide 20: STOBER encoder cables: assembly G5 / G6
Same assembly of encoder cables at G5 and G6
  Reduces cable diversity
  Concentrates the numbers of pieces
Only one connector type at drive controllers
Example: EnDat /SSI /Ink. encoder cable

## Slide 21: STOBER encoder cables: EnDat 2.1 / 2.2 digital with 5050044
Pairs (2 x 0,34 mm2): WH/BN, YE/GN, PK/GY
Pairs (2 x 0,25 mm2): RD/BU
Encoder connector con 15 / con 17 and con 23, 12 pins
Connector drive controller D-Sub 15 (X4)
Data +
Data -
Clock +
Clock -
U2 / U2BAT-
0V GND
U2 Sense / U2BAT+
Sketch encoder cable 5050044 (49484) EnDat 2.1 / 2.2 digital

## Slide 22: STOBER power cable – internal structure
U
V
W
PE
5
6
7
8
Power: U (1), V (2), W (3), PE
Brake: 5 (1BD1), 6 (1BD2)
Thermal sensor: 7 (1TP1), 8 (1 TP2)
Outer shield
Shield of pairs

## Slide 23: STOBER power cable – internal structure /2
Real: (4 × 1,5 + (2 × 1,0) + (2 × 0,50)) mm²

## Slide 24: Rated currents power wires
Design according to DIN VDE 0298-4 use of cables and insulated lines for power installations; part 4: Recommended values for the current-carrying capacity of cables and lines for fixed installation in buildings and of flexible lines
New definition of the rated currents in 2021
This allows a range of EZ engines to be offered with more competitive cables
    Cheaper
    Lighter
    More flexible
Current carrying capacity of conductors based on DIN VDE 0298 T4 06/13
Table 11: Load capacity, cables with rated voltage up to 1000 V and heat-resistant cables
  Column 5: on or at surfaces; multicore cables
Table 17: Conversion factors for deviating ambient temperatures
  Column 4: Factor (e.g. 40°C – 0,87)
Table 21: Conversion factors for accumulation on the wall, in the pipe and duct, on the floor and under the ceiling  Note in the connection method manual

## Slide 25: SAP Variant Configurator – selection power cables
Already updated
1 mm2 cable has to be checked at motors with brake and cable length e.g. > 25 m
  Voltage drop

## Slide 26: Assignment to EZ servo motors – connector / cross section
Size of the connector and minimum cross section of the cable
EZ motors for convection cooling IC 410

## Slide 27: Assignment EZ servo motors – applications
Verification of minimum cross section
  Standstill current I0 of the motors
  Permissible current carrying capacity of the conductors
    Basic requirements for the wiring of machines: DIN EN 60204-1:2007-06
    Detailed informations: DIN VDE 0298-4:2013-06
  Cable length
    Cable length of the power cores has an influence on the possible short-circuit currents, which must be controlled by the device fuse protection
    Cable length of the brake cores can cause problems due to a voltage drop
  Terminal specifications of the drive controller or output choke
  Connector size of the motors

## Slide 28: Cable selection suitable for drive controller series / CS
Power cables con 40
Extension cables

## Slide 29: Selection of the assembled power cable

## Slide 30: OCS – One Cable Solution
OCS hybrid cable Gen. 2.1
Power
EnDat 3 / HIPERFACE DSL
PTC / Pt1000
SI6 / SC6 / SB6 (E2101)
EZ motors
EnDat 3

## Slide 31: STOBER OCS hybrid cable – sketch inner structure
U
V
W
PE
5
6
wh
bu
Power: U (1), V (2), W (3), PE
Brake: 5 (1BD1), 6 (1BD2)
Encoder: wh (P_D+), bu (P_D-) – EnDat 3
Outer shield
Pairs
shield
SI6 / SC6 / SB6 (E2101)
There is a lot of STÖBER know how in this cable!

## Slide 32: STOBER OCS hybride cable – cross sections
For the "restart" of the OCS version, initially only two cable variants of generation 2.1 were introduced
5050030; (4G 1,5 + (2 x 0,75) + (2 x AWG22)); max. Ø 14,7 mm; weight 0,315 kg/m
5050031; (4G 2,5 + (2 x 0,75) + (2 x AWG22)); max. Ø 16,8 mm; weight 0,4 kg/m
Only OCS cables with connector size con 23 available
Technical framework for use in energy chains
  10 x D free to move
  5 m/s2 up to 20 m travel path
  5 mio. bending cycles
  4 m/s travel velocity
  Torsion max +/-30°/m
Raw cable with CURUS
Operation of motors up to size EZ705U_140 possible
Hybride cable Gen. 2.1 (4x2,5 + (2x0,75) + (2xAWG22))

## Slide 33: STOBER connection method manual – Contents
Compendium for STÖBER system cables
Detailed illustration of the encoder, power and OCS hybrid cables
Technical data
Sizing aid with reference to standards
Overview preassembled cables (Catalog products in 2,5 m up to 100 m)
Terminal specifications with indication of stripping length
Tables of service packs for power and encoder connectors
Interface adapters for encoder cables