## Slide 1: STOBER goes PROFIdrive
Implementing motion control applications with STOBER and Siemens
User's choice

## Slide 2: STOBER system advantages now also with PROFIdrive
Benefit from the advantages of the STOBER drive system made up of
gear units,
motors,
drive controllers and cables.
In combination with a SIMATIC controller. For quick success and demanding movement. In any industry. For any application.

## Slide 3: STOBER system advantages now also with PROFIdrive
Rack and pinion drives with the highest gearing quality.
High-quality helical gearing for low noise development and the best smooth operation.
Low-backlash planetary gear units for µm-precise positioning and maximum torsional stiffness.
Large selection of coaxial and right-angle gear units.
High gear ratio variance for the best possible optimization of mass inertia ratios.
Compact geared motors that are directly attached.
Super-compact synchronous servo motors.
High-performance drive controllers with numerous certified safety functions.
With a modular design
and freely scalable

## Slide 4: Your partner for demanding movement
Practical system solutions for drives and automation since 1934.
15,283 possible combinations of gear units and motors.
Numerous one-of-a-kind technology highlights and project-related adjustments.
Expert support during drive configuration and commissioning included.
International availability and global service.

## Slide 5: Motion control: Intuitive. Efficient. Trusted. Programming.
Implement the most complex motion control (MC) applications yourself with STOBER, PROFIdrive and the engineering framework for all automation tasks – the TIA Portal.
PROFIdrive: One profile – six application classes.
Class AC1: Standard drives (pumps, fans, stirrers, etc.).
Class AC2: Standard drives with technology functions.
Class AC3: Positioning drives.
Class AC4: MC drives with central, higher-level MC intelligence and patented "Dynamic Servo Control" position control concept.
Class AC5: MC drives with central, higher-level MC intelligence and set position value interface.
Class AC6: MC drives with decentralized MC intelligence integrated into the drives.
For a huge range of applications.

## Slide 6: Motion control in focus: PROFIdrive and MC intelligence …
Decentralized control and positioning – MC intelligence in the drive!
Drive connection using function blocks (FB)
Proven code blocks with standardized interfaces.
3 function blocks handle the communication to the drive controller (PROFIdrive over PROFINET)
  Connection of a speed-controlled axis using FB SINA_SPEED.
  Connection of a position-controlled axis using FB SINA_POS.
  Cyclical communication using FB SINA_PARA.

## Slide 7: Motion control in focus: PROFIdrive and MC intelligence …
Central control and positioning – MC intelligence in the controller!
Speed axis
Positioning axis
Synchronization
Drive connection using technology objects (TO)
Represent the mechanical components.
Encapsulate the technical functionality.
Form a standardized interface between the software and hardware
9 technology objects handle the communication to the drive controller (PROFIdrive over PROFINET)
  Speed axis: TO_SpeedAxis
  Positioning axis: TO_PositioningAxis (TO_BasicPos)
  Synchronous axis: TO_SynchronousAxis
  External encoder: TO_ExternalEncoder
  Measuring gauge: TO_MeasuringInput
  Cam: TO_OutputCam
  Cam track: TO_CamTrack
  Cam disk: TO_Cam
  Kinematics: TO_Kinematics

## Slide 8: Intuitive, powerful and free!
STOBER supports the PROFIdrive motion control functions of the TIA Portal:
Intuitive, powerful and free!
We help you ...
program motion control solutions efficiently.
with reusable results.
time-saving.
with the highest project quality.

## Slide 9: STOBER & PROFIdrive step 1: Functions in firmware V6.5-D or later
Application class | Application | Drive connection | Communication frame
AC1 Standard drives | Speed control with set speed value Pumps, fans, stirrers, conveyor belts | FB SINA_SPEED TO_SpeedAxis | 1 1,2,3
AC3 Positioning drives | Drive-based positioning: Position control without interpolation/kinematics | FB SINA_POS TO_BasicPos | 111
AC4 MC drives with central, higher-level MC intelligence | Controller-based positioning: Positioning, synchronous position operation, cam disk, interpolation/kinematics | TO_PositioningAxis TO_SynchronousAxis TO_CAM TO_Kinematics…. | 3,5,102,105

## Slide 10: Class AC1: Speed control with set speed value via FB
Drive connection using function block FB SINA_SPEED
Frame 1. Proven technology (available for > 10 years), open-source function block.
For all applications that do not require any positioning: Pumps, fans, stirrer, etc.
Available since firmware V6.5-D (July 2021).

## Slide 11: Class AC1: Speed control with set speed value via TO
Drive connection using technology object TO_SpeedAxis
Frame 1, 2 or 3.
For all applications that do not require any positioning.
Available since firmware V6.5-D (July 2021).

## Slide 12: Class AC1: Speed control with set speed value via FB
Drive connection using function block FB SINA_POS
Frame 111. Proven technology (available for > 10 years), open-source function block.
Position control in the drive controller, excellent quality even with low-priced CPU.
Available since firmware V6.5-D (July 2021).

## Slide 13: Class AC3: Position control via TO
Drive connection using technology object TO_BasicPos
Frame 111.
Position control in the drive controller, excellent quality even with low-priced CPU.
Available since firmware V6.5-D (July 2021).

## Slide 14: Class AC4: Position control with set speed value with IRT via TO
Drive connection using technology objects TO_PositioningAxis, TO_SynchronousAxis, TO_CAM and TO_Kinematics
Frame 3.
Synchronous position operation, cam disk, interpolation, transformations.
Best performance with IRT and T-CPU.
Available since firmware V6.5-F (April 2022).

## Slide 15: Class AC4: Position control with set speed value with IRT via TO
Drive connection using technology objects TO_PositioningAxis, TO_SynchronousAxis, TO_CAM and TO_Kinematics
Frame 5, 102 or 105.
Synchronous position operation, cam disk, interpolation, transformations.
Highest performance due to DSC. (Position control in the drive).
Available since firmware V6.5-J (April 2023).

## Slide 16: STOBER goes PROFIdrive: Facts & benefits
Standardized interfaces for STOBER SC6 and SI6 drive controllers.
  Standardized cyclical mappings.
  Convenient commissioning: Controller determines the properties of the drive using defined PROFIdrive objects.
Straightforward drive controller replacement.
  Drive controllers in configured applications can easily be replaced in the TIA Portal without changing the program.

## Slide 17: STOBER goes PROFIdrive: Facts & benefits
Reusable software components.
  Software components can be used directly within applications regardless of manufacturer, thanks to the programming of the technology objects in accordance with PLCopen or the use of DriveLib function blocks.
Simulation.
  Axes can be simulated without using the corresponding hardware; the CPU utilization can be calculated in advance.
Applications.
  Numerous application templates available: winder, flying saw, rotating shear, conveyor tracking, kinematics, etc.